## Slide 1: OSI MODEL
Computer Networks

## Slide 2: OSI MODEL
The OSI model is a framework containing seven layers that defines the protocols and devices used at each stage of the process when data travels through a network
As data is packaged to be sent out to the network it travels from the Application Layer (layer 7) to the Physical Layer (layer 1)

## Slide 3: The Physical Layer (Layer 1)
Layer Notes | System Profile
What does the physical layer do? Includes all the physical tangible parts of the network that can be touched – cables, devices, electric signals Cannot interpret signals – no intelligence What protocols or devices does it use? Cables, hubs, repeater, Network interface card (NIC) Note: NIC also functions at the Data Link Layer (Layer 2) | Locate information about your network adapter: Your MAC address: Device type: Location:
SEE HANDOUT TO COMPLETE SYSTEM PROFILE INFORMATION

## Slide 4: Data Link Layer (Layer 2)
Layer Notes | System Profile
What does the data link layer do? Media Access Control (MAC) Provides MAC addresses to computers Translates data bits going from the NIC to the cable from hexadecimal values into binary Logical link control (LLC) Acts as a buffer. Stores information being sent out to the cables and sends it piece by piece. Checks for errors in information being sent by using a checksum. | Translate your hexadecimal MAC address to binary, and then to decimal. Binary: Hex: Decimal: Type MAC address into calculator (do not include dashes). Write the Binary, Hexadecimal and Decimal numbers above.
Go to
http://easycalculation.com/hexconverter.php

## Slide 5: Data Link Layer (Layer 2)
Layer Notes | System Profile
What protocols or devices does the data link layer use? Switch: controls flow of data coming from one computer’s MAC address and directs it to the next MAC address destination. Bridge: Controls data flowing between two local network segments Network Interface Card (NIC): translates the hexadecimal values into a binary electric signal and translates incoming signals back to hexadecimal | 

## Slide 6: Network Layer (Layer 3)
Layer Notes | System Profile
What does the network layer do? Handles the routing of data across the network or other destination networks. Controls the Internet Protocol addresses (IP addresses) assigned by DHCP What protocols or devices does it use? Routers: used to divide large LANs into smaller segments or for home network to access the Internet. Gateway: used in larger networks to connect LAN to the Internet Firewalls: Routers and gateways serve as a perimeter firewall and block traffic based on IP addresses | Use ipconfig to find your IP address. Go to command prompt and type in ipconfig. Write your IP address here.

## Slide 7: Transport Layer (Layer 4)
Layer Notes | System Profile
What does the transport layer do? Allows sender and receiver to establish a connection in order to send data provides acknowledgement when a message is received Checks for errors and resends data if necessary Two types of Transport protocols: TCP (Transmission Control Protocol) and UDP (User Datagram Protocol) | Open a web browser and visit a few websites in different windows. Leave the websites open. Go to command prompt. Type in netstat –n to check network status. The out put will show all the IP addresses of websites you’re connected to. List all foreign IP addresses here.

## Slide 8: Transport Layer (Layer 4)
Layer Notes | System Profile
What protocols or devices does the transport layer use? TCP: Packages packets for sending, checks them as they arrive, and puts them in order (called sequencing) Flow control: The transport layer controls the bitstream once it’s on the Net. | 

## Slide 9: Session Layer (Layer 5)
Layer Notes | System Profile
What does the session layer do? Sets up a connection for an ongoing “session” for an application (e.g. instant messaging) Two sides agree to rules such as: speed, protocols, encryptions used. Known as “handshake” Manages the session and terminates it | 

## Slide 10: Session Layer (Layer 5)
Layer Notes | System Profile
What protocols or devices does the session layer use? Instant Messaging (IM) Online real-time games | What programs on the computer initiate a session as they connect? Homework Load an IM session and describe the process as it is connecting. It hooks in to the server where other people are logged in, authenticates, and establishes the connection. IM another student in the class. Is there a lag? Why or why not?

## Slide 11: The Presentation Layer (Layer 6)
Layer Notes | System Profile
What does the presentation layer do? Controls how the information is presented to the Application layer (layer 7) Translates binary data to ASCII Compresses data Controls encryption (https) What protocols or devices does the presentation layer use? Secure Sockets Layer (SSL) – websites that use log in portals use an SSL connection | How is the padlock system displayed in different browsers? Extra credit if you find out the answer.

## Slide 12: The Application Layer (Layer 7)
Layer Notes | System Profile
What does the application layer do? How the apps or software communicate with the network. (Example MS Word Help goes on internet) Controls authentication (log in and password) Determines whether enough resources such as memory and bandwidth are available | For extra credit: Find other examples of application layer applications

## Slide 13: The Application Layer (Layer 7)
Layer Notes | System Profile
What protocols or devices does the application layer use? Internet browsers Desktop email Other Internet-going applications | 

## Slide 14: The OSI Seven Layer Model
Mnemonics for Memorization
Please Do Not Throw Sausage Pizza Away
A Perfect System That Never Did Look Perfect
All People Seem To Need Data Processing
Please Do Not Take Sales People’s Advice